Pressure Sensor [component]
Test Case: 1.1001 Sensing presence or lack of pressure
This test ensures that the component and wiring can determine the presence or lack of pressure.

Procedure:
Push on the pressure sensor	Current flows through to uC
	uC lights up LED connected to separate pin
Release force on pressure sensor	Current stops flow, or lower flow, to uC.
	uC turns off LED connected to same pin

 Pass/trials: 20/20

Pressure Sensor [component]
Test Case: 1.1002 Accuracy of Pressure ( it should detect varying pressure accuracies)
This test ensures that the component is sending an analog signal so that the aref is used for the varying pressures.

Prerequisite tests: Test Case: 1.1001 Sensing Presence or Lack of Pressure

The uC is wired such that port A has 8 LEDs attached and outputs the pressure value on port A. Port B has the pressure sensor is properly wired to it.	The system is ready for the test.
The pressure sensor has no pressure added.	All LEDs are off.
Light or soft pressure is added to the sensor.	The first 1 to 4 LEDs turn on projecting its pressure value.
Medium pressure is acted on the sensor.	The fifth to eighth LEDs light up, but on the higher values, there are not that many lights on.
Large pressure is acted on the sensor.	Nearly all of the LEDs light up.

Pass/Trial: 10/10

Electromagnet [component]
Test Case: 2.1002 Necessary Electromagnetic Force
This test ensures that the electromagnet applies the enough force required.
Prerequisite Test(s): Test Case: 2.1001 Electromagnetic Force
Test Case 3.1003 Electromagnetic Sensor

Wire the electromagnet to the uC on Port B.
Turn on the uC.	The electromagnet turns on.
The electromagnet is positioned an inch from a paper clip.	The electromagnet picks up the paper clip.

Pass/Trials: 10/10